## Slide 1: Underground Support System Limitations
Ryan C. Stephan, P.E.
Mechanical Engineer
MSHA- Technical Support
Roof Control Division
412-386-6314

## Slide 2: Outline
Load Expectations
Standing Support Characteristics
Wood Crib Best Practices
Pumpable Crib Best Practices
New Standing Support Product
Roof Beam Deflection Demonstration

## Slide 3: Standing Support Load Requirements
Pillar Loads
Roof Load
Notes: Can’t stop global convergence
Want to control local roof load

## Slide 4: Standing Support
Mains
Longwall Tailgate
Bleeders
Belt Drive
Notes: Discuss how much movement may be expected in each area
More abutment loading = more convergence = deteriorating roof conditions
Different support types
Different expected convergence/ abutment load

## Slide 5: Outline
Load Expectations
Standing Support Characteristics
Wood Crib Best Practices
Pumpable Crib Best Practices
New Standing Support Product
Roof Beam Deflection Demonstration

## Slide 6: Properties of Roof Supports
Yield/peak capacity
Stiffness
Residual characteristics
Convergence Range
The following data was collected by NIOSH through full scale testing

## Slide 7
Notes: 3,000,000 pounds vertical
1,600,000 pounds horizontal
8,800 tests since 1981

## Slide 8: Load vs. Displacement
100-ton Prop
100-ton Prop
Link-N-Lock
36-inch Link-N-Lock
Support Load, tons
Displacement, inches
Notes: First question is usually “How much load can the support carry” = capacity
Explain chart- load vs displacement…
Depends on- configuration, materials, and height
Peak capacity = Link N Lock = 2X jack
If you don’t want any movement…Jack is better
Load @ 1/4” … Jack= way stronger

## Slide 9: Support Stiffness
Standing supports develop their load-carrying capacity only through roof movement
A measure of how quickly a support system develops its load carrying capacity in response to convergence

## Slide 10: Capacity vs. Stiffness
Capacity = How much load can the support carry
vs.
Stiffness = How much load can the support carry
at a specified amount of displacement?

## Slide 11: Support Stiffness
Support Type | Initial Stiffness (tons/inch)
4-Point Crib | 23
12’ Cable Bolt | 38
9-Point Crib | 54
8-12” Post | 112
Fiber Crib Column | 221
24” Pumpable Crib | 234
100-ton Prop | 485

## Slide 12: Residual Load
The behavior of a support after peak capacity is exceeded
Notes: Discuss longwall tailgate

## Slide 13: Residual Load
24-inch Pumpable Crib
100-ton Prop
24-inch Pumpable Crib
24-inch CAN
100-ton Prop
Support Load, tons
Displacement, inches
24-inch CAN
Notes: Residual Load = behavior of a support after peak capacity is exceeded

## Slide 14: Convergence Range
The total amount of convergence of the support until the support has declined to 40% of its peak load capacity
Notes: NIOSH determined 40% as arbitrary cutoff – still can be usefulness after that…

## Slide 15: Convergence Range
10-inch Propsetter
8-inch Wood Post
Support Load, tons
Displacement, inches
Propsetter

## Slide 16: Convergence Range
Support Type | Convergence Range (inch)
100-ton Prop | 1
Fiber Crib Column | 2
8-12” Post | 3
10” Propsetter | 13
24” Pumpable Crib | 19
9-Point Crib | 20
4-Point Crib | 22

## Slide 17: Stiffness vs. Convergence Range
Support Type | Initial Stiffness (tons/inch) | Convergence Range (inch)
100-ton Prop | 485 | 1
Fiber Crib Column | 221 | 2
8-12” Post | 112 | 3
10” Propsetter | 71 | 13
24” Pumpable Crib | 234 | 19
9-Point Crib | 54 | 20
4-Point Crib | 23 | 22

## Slide 18: Other Factors
Stability
Material handling requirements
Installation Quality
Timing
Skin Control
Notes: Material handling – 5,000 workdays lost each year from timber handling…

## Slide 19: Outline
Load Expectations
Standing Support Characteristics
Wood Crib Best Practices
Pumpable Crib Best Practices
New Standing Support Product
Roof Beam Deflection Demonstration

## Slide 20: Timber Overhang
Overhang timbers by half of the timber width
6”
3”
3”

## Slide 21: Timber Orientation
7-inch Wide Timber
7-inch Tall Timber
Notes: Cribs constructed of 5x7” timbers
Capacity, stiffness, residual load, convergence range

## Slide 22: Aspect Ratio
Maximum Aspect Ratios (H/W):
  4-Point Wood Crib: 4.3:1
  Concrete Crib: 6.0:1
  CAN: 5.0:1
  Pumpable Crib: 5.0:1
W
H
Notes: What does this look like for 4-point crib?

## Slide 23
Aspect Ratio ~ 4.3:1
Notes: ~Maximum height
30-inch timbers
6.5-7 feet tall

## Slide 24
Aspect Ratio ~ 9.3:1
Notes: Does this seem within aspect ratio?
Also, Minimal overhang

## Slide 25: 4-Point Crib Height
Maximum Crib Height (6x6 blocks)
Timber Length (inches) | Maximum Crib Height
24 | 4’ 4”
30 | 6’ 6”
36 | 8’ 7”
42 | 10’ 10”
48 | 12’ 11”
Notes: Good chart to keep on hand

## Slide 26: Outline
Load Expectations
Standing Support Characteristics
Wood Crib Best Practices
Pumpable Crib Best Practices
New Standing Support Product
Roof Beam Deflection Demonstration

## Slide 27: Pumpable Crib Best Practices
Proper Installation:
  Within aspect ratio
  Plumb
  Damage to bag repaired
  Roof contact
  Slightly pre-stressed
Notes:   Cut-able cribs have about half the peak and residual capacity. Same convergence range

## Slide 28: Pumpable Crib Best Practices
 | RCD
Max Aspect ratio | 5:1
Max bow/tilt | 25% of Diameter
Wood Base | Until aspect ratio is below 5:1
Capacity | De-rated based on aspect ratio

## Slide 29: Installed Off-Plumb
10% of height
25% of diameter
Notes: 5:1 aspect ratio

## Slide 30: Pumpable Crib Best Practices
 | RCD
Max Aspect ratio | 5:1
Max bow/tilt | 25% of Diameter
Wood Base | Until aspect ratio is below 5:1
Capacity | De-rated based on aspect ratio

## Slide 31: Outline
Load Expectations
Standing Support Characteristics
Wood Crib Best Practices
Pumpable Crib Best Practices
New Standing Support Product
Roof Beam Deflection Demonstration

## Slide 32: Gorilla Support
Manufactured by MICON
Diameters ranging from 8 to 20 inches
7.2:1 Maximum Aspect Ratio
Corrugated tube filled with bamboo and polyurethane
Lightweight and requires minimal labor to install

## Slide 33: Gorilla Support
Manufactured by MICON
Diameters ranging from 8 to 20 inches
7.2:1 Maximum Aspect Ratio
Corrugated tube filled with bamboo and polyurethane
Lightweight and requires minimal labor to install

## Slide 34: Gorilla Support
Gorilla Support

## Slide 35
Gorilla Support
12-inch Gorilla Support
10-inch Propsetter
Support Load, tons
Deflection (inches)
Gorilla Support
Notes: You may ask…”Is that any good?”
It depends on what you compare to

## Slide 36: Outline
Load Expectations
Standing Support Characteristics
Wood Crib Best Practices
Pumpable Crib Best Practices
New Standing Support Product
Roof Beam Deflection Demonstration

## Slide 37: Roof Beam Deflection Example

## Slide 38: Roof Beam Deflection Example

## Slide 39: Standing support – Soft vs stiff
Soft Support
Stiff Support

## Slide 40: Standing support – Soft vs stiff
Soft Support
Stiff Support

## Slide 41: Summary
Load Expectations
Standing Support Characteristics
Wood Crib Best Practices
Pumpable Crib Best Practices
New Standing Support Product
Roof Beam Deflection Demonstration

## Slide 42: Questions
Ryan C. Stephan, P.E.
stephan.ryan@dol.gov
412-386-6314